San Diego Audio Hackers
Spectrograms Explained
July 10, 2016
Nick Hilton

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
Time domain signals
- List of values
  - {time, amplitude}, {time, amplitude}, ...

---
Time domain signals
- List of values
  - {time, amplitude}, {time, amplitude}, ...

---
Time domain signals
- List of values
  - {time, amplitude}, {time, amplitude}, ...

---
Time domain signals
- List of values
  - {time, amplitude}, {time, amplitude}, ...

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
Frequency domain signals
- List of values
  - {frequency, amplitude}, {frequency, amplitude} ...

---
Frequency domain signals
- List of values
  - {frequency, amplitude}, {frequency, amplitude} ...

---
Frequency domain signals
- List of values
  - {frequency, amplitude}, {frequency, amplitude} ...

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
How to make spectrograms
Recipe
  1. Break up input signal into frames
  2. Apply a window to remove step function at edge
  3. Transform frame into frequency domain via FFT
  4. Place frequency domain frame into spectrogram matrix

---
1
3
4
2

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
The Heisenberg uncertainty principle
Formula
- Meaning for signal processing
  - You can't know frequency & time precisely simultaneously
%DELTA x %DELTA p >= { h } over { 4 %pi }

---
The Heisenberg uncertainty principle
When is the signal 3 Hz?

---
The Heisenberg uncertainty principle
When is the signal 3 Hz?

---
The Heisenberg uncertainty principle
When is the signal 3 Hz?

---
The Heisenberg uncertainty principle
When is the signal 3 Hz?

---
The Heisenberg uncertainty principle
- We must process finite duration of the signal
  - So we reduce the amount memory used
  - But more importantly, so we can know approximately when the signal contains which frequencies

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits the minimal observable frequency

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits the minimal observable frequency

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits the minimal observable frequency

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits if two close two tones can be resolvable

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits if two close two tones can be resolvable

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits if two close two tones can be resolvable

---
The Heisenberg uncertainty principle
Choosing a finite “window”
  1. Limits if two close two tones can be resolvable

---
The Heisenberg uncertainty principle
- A trade off must be made
  - Time resolution
  - Frequency resolution
  - You can't have both!

---
Outline
- Time domain signals
- Frequency domain
- How to make spectrograms
- Heisenberg uncertainty principle
- Spectrograms

---
Spectrograms